What do the colour codes on the 6L6 and EL34 Poweramp tubes mean? (GRY,GRN,YEL,RED,BLU...)

The reason for the classification is to enable a most precise matching of Tube pairs used in Push-Pull output circuits, therefore these Tubes are allways offered in pairs. When exchanging Tubes in MESA/BOOGIE amps the original colour is of no importance, nor does it have an effect on the sound.

Push-Pull means that two Tubes are on one circuit and this is where the only requirements lay ref. the colour code: Two biased tubes must allways have the same colour ( no matter which colour). In an amp with two tubes you can simply exchange the old tubes for a new pair.

With amps with more than one pair of tubes we can go even further: In a Dual Rec Solo Head for example there are two pairs of tubes. The tube pair in the middle work together as do the two outside tubes ( from left to right tubes 1+4 res. 2+3 ) When exchanging the tubes, a RED pair can be used in the middle sockets and a BLUE pair in the outer sockets. Due to the extremely low tolerances, this can be carried without any loss of power or sound quality.